SITE-FABRICATED STRETCHED FABRIC WALL AND CEILING SYSTEMS

LEED/SUSTAINABLE PROJECTS

SYSTEM DESCRIPTION

- Site-fabricated stretched fabric panel system with continuous perimeter track profile mounted directly to sheetrock substrate. System shall provide for face fabric to be perfectly tensioned over core materials, leaving fabric floating over core surface.

- System will allow for the removal and replacement of fabric facing from individual panels. Removal of fabric shall allow access to surface behind fabric without dismantling, removal or replacement of track members or core.

- Prefabricated panels or wood ground systems do not satisfy the intent of this specification.

ACCEPTABLE MANUFACTURER/AUTHORIZED DISTRIBUTOR/CERTIFIED INSTALLER

- NOVAWALL( as manufactured by

Novawall Systems, Inc.,

885-B South Picket Street

Alexandria, Virginia 22304

(800) 695-6682

(703) 461-0113

(703) 461-0436 fax

Website: www.novawall.com

Email: sales @novawall.com

- Authorized Distributor or Certified Installer

(Territory map at  www.novawall.com  or consult with a Novawall( representative)

SYSTEM COMPONENTS

- Novawall( Perimeter Edge Track - extruded polymer edge track profiles required to conform to panel edge detail desired – select one or two types and thickness:

(½” Square-Universal Edge) (½” Square-Universal Edge) (½” Square-Universal Edge)  (1” Square-Weltless Edge) (1” Square-Concealed Edge)  (1” Square-Classic)

(1” Square-¼” Reveal Edge) (1” Square- ½” Reveal Edge) (1” Bevel) (1” Radius)

(1” Square-Weltless EcoTrack – PVC Free)

- Novawall( Midwall Track - select corresponding Novawall® midseam panel joint:

(½” Square-Butt Joint) (1” Square-Butt Joint) (1” Square-⅛” Reveal Insert)

(1”Square-¼” Reveal) (1” Square- ½” Reveal) (1” Bevel Midwall) (1” Radius Midwall) (1” Square-EcoTrack Butt Joint – PVC Free)

- Core materials:

Acoustical: Fiberglass Rigid (½” Thick 6 pcf density) (1” Thick 6 pcf density)

- Acoustical Core Material : Fiberglass – Urea Formaldehyde Free

Rigid Fiberglass = Post Consumer Recycled Content/Greenguard Certified

  - Density: [6pcf.] [3pcf.]

  - Thickness: [1”][2”] nominal

  - Noise Reduction Coefficient; determined by ASTM C423 Type A Mounting:

[1) 1” thickness: .80 minimum]

[2) 2” thickness: 1.05 minimum]

2.	Acoustical Core Material : Novawall( Greenfill™

Novawall® Recycled Core= Post Consumer Recycled Content

- Density: [5.5pcf.]

- Thickness: [1”][2”] nominal

- Noise Reduction Coefficient; determined by ASTM C423 Type A Mounting:

[1) 1” thickness: .80 minimum]

[2) 2” thickness: 1.05 minimum]

Tackable/High Impact:

- Micore by US Gypsum [½” thick][¾” thick]

USG Micore=Post Consumer and Post Industrial Recycled Content

- Multi-density Fiberglass

(½” Multi-density fiberglass; 10-20 PCF)

(1” Multi-density fiberglass; 6 PCF density with ¼” 10-20 PCF face)

Fabric Selection:

Fabrics selected by Architect/Designer approved for intended end-use panel application by fabric manufacturer.

Note:	Fabrics with recycled polyester or sustainable content should be considered and can be calculated with Novawall’s version of ecoScorecardSM.

FP-1 [Manufacturer][Product Name][Style Number][Color][Fabric Width]

FP-2 [Manufacturer][Product Name][Style Number][Color][Fabric Width]

- Mounting Hardware:

Manufacturer’s standard fasteners for securing framing track directly to gypsum board, wood or plywood substrates. Pin nailing through fabric is not accepted.

INSTALLATION

- Fabricate panel system on jobsite to conform precisely to existing conditions in areas indicated for their application. Space shall be enclosed and weather-tight.

- Apply framing materials to sheetrock surfaces scheduled to receive system.   Framing shall be plumb and straight, flush, and in proper alignment.  Mounting channel details and core coloration shall not be visible through facing fabric.

- Core materials shall be installed in a continuous manner, flush and level with framing materials. Core materials shall not “telegraph” through the face fabric.

- Cut fabric from each roll maintaining a regular sequence of drops and matching direction of weave for sequential and uniform installation.

- Fabric shall be tensioned securely to track system using appropriate tools.  Spray adhesives or stapling of fabric to core or frame members shall not be permitted.

- Clean exposed surfaces of wall fabric.  Trim and remove loose threads.  Remove surplus materials, rubbish, and debris, leaving area neat and in a clean condition.

LEED/Sustainable Submittals

1. 	Submit LEED credit calculations and required paperwork and certification items for review by LEED committee. Version of LEED project required.

Note:	Novawall Systems, Inc. will provide preliminary and final LEED credit calculations using the customized software version of ecoScorecardSM. Project calculations using the ecoScorecardSM program can only be used for a Novawall( system and must be certified by a Novawall Systems, Inc. representative.

2.	Materials and Resources

a. 	Credit 4 Recycled Content

Note:	Novawall( systems are comprised of three components: face fabric, core material and polymer extrusions. Many choices of face fabric or core materials will have varying degrees of recycled content. For example; Novawall( Greenfill™ is a 5.5 pcf. Acoustic board and 100% post consumer recycled content.

b.	Credit 5 Regional Materials 20% Manufactured Regionally (LEED CI Only)

Note:	Novawall( products are site fabricated by local trained and qualified installers.

c. 	Credit 6 Rapidly Renewable Materials

Note:	Novawall( offers core material that may provide a contribution to this credit. There are also fabrics manufactured from Bio-based materials that may contribute to this LEED credit.

3.	Indoor Environmental Quality

a.	Credit 4.1 Low-emitting Materials, Adhesives and Sealants

Note:	Novawall( systems are designed to be installed without  need for adhesives and sealants. This provides an advantage to indoor air quality due to the fact that that there are no VOC’s added to the building from chemicals that are typically associated with installation of wall and ceiling coverings. Core materials should always be a consideration for Indoor Air Quality and consider Urea Formaldehyde Free products that may be Greenguard Certified.

## MANDATORY FIRE CODE COMPLIANCE/ACOUSTICAL TESTS

- This fire code section is considered mandatory. Stretched fabric panel systems or fabrics not in compliance should be rejected.

- Submit complete, unedited test reports for stretched fabric panel system prepared by an independent testing laboratory that is IAS Certified indicating full compliance with fire resistance performance requirements under ASTM E84 and specifically;

- Fire ratings shall be for a complete assembly, including perimeter and longitudinal butt joint framing extrusions, core material, and fabric covering as required by ASTM E2573-07 Specimen Preparation and Mounting of Site Fabricated Stretch Systems to Assess Surface Burning Characteristics.

- Systems must be certified under ASTM E84 and Class must be compliant with placement in the building:

Class A with a Flame Spread Index (0-25) Smoke Developed Index (0-450)

Class B with a Flame Spread Index (26 - 75) Smoke Developed Index (0-450)

Class C with a Flame Spread Index (76 – 200) Smoke Developed Index (0-450)

- Submit complete test reports for each fabric prepared by an independent testing laboratory that is IAS Certified indicating compliance with specified fire resistance performance requirements under ASTM E84 Unadhered Method.

- ASTM C423 Test Method for Sound Absorption and Sound Absorption Coefficients by Reverberation Room Method

(NRC for 1” system:  0.80)(NRC for 2” system:  0.95)(NRC for 4” system:  1.05)

## LIMITED LIFETIME WARRANTY*

A.	Stretched fabric panel system installation shall be warranted by the Authorized Distributor or Certified Installer for the period defined in contract documents.

B.	Novawall® provides a Limited Lifetime Warranty* to the Authorized Distributor or Certified Installer for the “Life” of the installation.

*Novawall® will provide replacement Novawall( extrusions that are deemed defective at no charge to the Authorized Distributor or Certified Installer during the “useable life” of an installation. Novawall® does not warranty against damage by others, normal wear and tear, the project installation, fabric or core materials which may have certain other manufacturer warranties.

C. 	EcoTRACK® extrusions have a Five (5) Year Warranty by Novawall® to the Authorized Distributor or Certified Installer.

*Novawall® will provide replacement Novawall( EcoTRACK® extrusions that are deemed defective at no charge to the Authorized Distributor or Certified Installer during the 5 Year Warranty period. Novawall® does not warranty against damage by others, normal wear and tear, the project installation, fabric or core materials which may have certain other manufacturer warranties.